## Slide 1
SMART INHALO
Hybrid ML + DL Breathing Technique Classification
From real respiratory signals to Correct / Wrong technique labels
and a deployable hybrid machine-learning model
Dataset Pipeline · Technical Labeling · Model Comparison · Deployment

## Slide 2
AGENDA
01
Problem & Motivation
Why inhaler technique matters
02
Project History
How the work evolved
03
Data Source
PhysioNet respiratory dataset
04
Dataset Pipeline
From raw signals to cycle features
05
Technical Labels
Correct / Wrong proxy construction
06
Modeling Approach
Hybrid classical ML + deep learning
07
Results & Safeguards
Metrics, leakage controls, deployment
08
Next Steps
Real inhaler audio & product path

## Slide 3
THE PROBLEM
Incorrect inhaler technique is extremely common and reduces drug delivery.
Poor adherence
Many patients use inhalers incorrectly without knowing it.
No real-time feedback
Clinicians cannot watch every dose at home.
Outcome impact
Wrong technique leads to less drug in the lungs and worse asthma / COPD control.
Opportunity
Sensors + ML can score technique automatically from breathing signals or audio.

## Slide 4
PROJECT GOAL
Classify each breathing cycle as Correct or Wrong technique
using real respiratory measurements and a hybrid ML + DL stack.
1
Build dataset
Extract clean cycle-level features from PhysioNet multi-channel signals.
2
Create labels
Define a transparent technical Correct / Wrong proxy without clinician labels.
3
Train models
Compare Logistic Regression, Random Forest, SVM, and MLP under subject split.
4
Deploy safely
Save model + scaler + feature order as one inference bundle.

## Slide 5
PROJECT HISTORY — HOW THE WORK EVOLVED
1
Signal exploration
Loaded PhysioNet subject files; inspected flow, pressure, volume, chest and abdomen belts.
2
Cycle extraction
Used inspiratory indices to segment continuous recordings into individual breathing cycles.
3
Feature engineering
Computed peak / min / mean / range / std for flow and pressure; tidal volume; belt ranges.
4
Quality control
Removed non-physiological cycles (extreme duration, near-zero flow/pressure, dead sensors).
5
Master table
Built respiratory_master_dataset.csv — 13,137 clean cycles from 79 subjects.
6
Technical labels + ML
IQR abnormality score to Correct/Wrong; trained hybrid models; saved deployable bundle.

## Slide 6
DATA SOURCE — PHYSIONET RESPIRATORY DATASET
80
Subjects recorded
79
Subjects retained
13,137
Clean breathing cycles
5
Signal channels
Channels used
Flow [L/s]
Pressure [cmH2O]
Tidal volume [L]
Chest belt [mm]
Abdomen belt [mm]
Subject groups (Trial Classification): Normal / Asthmatic / Smoker / Vaper x Male / Female
Public source: physionet.org/content/respiratory-dataset/1.0.0/

## Slide 7
DATASET PIPELINE
1
Raw signals
Download per-subject CSVs with inspiratory markers
2
Cycle cut
Segment between consecutive inspiratory indices
3
Features
Peak, min, mean, range, std for flow and pressure; volume; belts
4
QC filter
Drop duration <1s or >10s; near-zero flow/pressure; dead belts
5
Merge meta
Attach Trial Classification from subject-info
6
Label
IQR abnormality score to Correct / Wrong
Output: Smart_Inhalo_Master_Dataset.csv (26 columns, ready for ML)

## Slide 8
CYCLE-LEVEL FEATURES
Timing
- Cycle_Duration_s
Flow
- Peak / Min / Mean Flow
- Flow Range
- Flow Std
Pressure
- Peak / Min / Mean Pressure
- Pressure Range
- Pressure Std
Volume
- Max Tidal Volume
- Mean Tidal Volume
Belts
- Chest Range (mm)
- Abdomen Range (mm)

## Slide 9
QUALITY CONTROL RULES
Cycles are removed if they are physiologically implausible.
Duration < 1 s or > 10 s
Too short or too long to be a normal breath
Flow range < 0.5 L/s
Near-flat flow suggests sensor or segmentation error
Pressure range < 0.5 cmH2O
Insufficient pressure swing for a real cycle
Chest range = 0 AND Abd range = 0
Both belt sensors failed or disconnected

## Slide 10
TECHNICAL CORRECT / WRONG LABELS
No clinician-scored inhaler labels exist in this dataset.
We build a transparent technical proxy from signal statistics.
1
Select 6 features
Duration, Flow range, Pressure range, Max tidal volume, Chest range, Abd range
2
IQR band
25th-75th percentile = normal reference range for each feature
3
Flag abnormal
Feature outside the band becomes Abnormal = 1
4
Score and label
If Abnormal_Features >= 2 then Wrong, else Correct

## Slide 11
LABEL DISTRIBUTION
CORRECT
~2,224
cycles · ~17%
WRONG
~10,913
cycles · ~83%
Class imbalance is expected. Models use class_weight="balanced". Evaluation focuses on minority Correct and on Wrong detection.

## Slide 12
HYBRID MODELING APPROACH
Subject-wise train / test split (GroupShuffleSplit, 80/20)
No subject appears in both sets — the model must generalize across people, not memorize individuals.
Logistic
Regression
Linear baseline
interpretable
Random
Forest
Non-linear
no scaling needed
SVM
(RBF)
Strong kernel
boundary
MLP
(Deep Learning)
Neural net on
tabular features

## Slide 13
LEAKAGE SAFEGUARDS
Subject-level split
Train and test subjects are completely disjoint.
Label columns excluded
The 6 abnormality flags and Abnormal_Features never enter the model.
Clean input features only
Model sees flow / pressure / volume / belt statistics — not the label recipe.
Scaler fit on train only
StandardScaler is fit on training data; test is transformed only.
Inference bundle
Model + scaler + feature order + needs_scaling saved together for deployment.

## Slide 14
EXAMPLE MODEL RESULTS (SUBJECT SPLIT)
Model
Accuracy
Precision*
Recall*
F1*
Logistic Regression
0.66
0.39
0.88
0.54
Random Forest
0.97
0.99
0.89
0.94
SVM (RBF)
0.84
0.59
0.93
0.72
* Precision / Recall / F1 for the Correct class in one experimental run.
Random Forest often leads on tabular cycle features; ranking can vary with seed and feature set.
Best model is packaged with scaler + feature order into smart_inhalo_model.pkl for the app.

## Slide 15
WHAT WE DELIVERED
1
Smart_Inhalo_Master_Dataset.csv
13,137 cycles x 26 columns with Technique_Label
2
Dataset pipeline notebook
End-to-end extraction, QC, labeling — presentation-ready
3
Hybrid ML + DL notebook
Subject split, 4 models, metrics, ROC/PR, confusion matrices
4
smart_inhalo_model.pkl
Deployable bundle: model + scaler + feature list + label map
5
Predict API pattern
Single-cycle prediction function ready for mobile / web app

## Slide 16
LIMITATIONS & NEXT STEPS
Limitations
- Labels are a technical proxy, not clinician-scored inhaler technique
- Data are general respiratory signals, not inhaler-use events
- Class imbalance is strong (~17% Correct)
- Tabular features only — no raw waveform CNN yet
Next steps
- Train on real inhaler audio (ICBHI / RDA actuation datasets)
- Add 1-D CNN / LSTM on raw waveforms
- Collect labeled Smart Inhalo device data
- Ship mobile app using the .pkl inference bundle

## Slide 17
KEY TAKEAWAYS
01
Real signals, clean cycles
13k+ breathing cycles from 79 PhysioNet subjects after strict QC.
02
Transparent labels
IQR-based Correct / Wrong proxy — fully documented and leakage-aware.
03
Subject-safe modeling
Group split + excluded label columns + train-only scaler.
04
Hybrid models
Classical ML and MLP compared; best model saved for deployment.
05
Path to product
Same pipeline pattern applies when real inhaler audio labels arrive.

## Slide 18
THANK YOU
Questions & Discussion
Smart Inhalo · Hybrid ML + DL Breathing Technique Classification
PhysioNet Respiratory Dataset · Subject-safe pipeline · Deployable model